## Slide 1
Memory

## Slide 2: Introduction
Memory
  information storage
  a collection of cells store binary information
ROM – Read-Only Memory
  read operation only
  a programmable logic device
RAM – Random-Access Memory
  read operation
  write operation
2
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 3: Introduction
If memory has 2k words, k address bits are needed
  23 words, 3 address bits
Address locations are labeled 0 to 2k-1
Common subscripts:
  Kilo – 210
  Mega – 220
  Giga - 230
3

## Slide 4: Introduction
1M bits
1-bit
1-bit
220 memory cells
20
address lines
1M bits
8-bit
8-bit
217
memory cells
17
address lines
( 220x1 = 217x8 )
4
= 128 KB

## Slide 5: Read-Only Memory

## Slide 6: Read-Only Memory (ROM)
ROMs store permanent binary information
ROMs are effective at implementing truth tables
  Any logic function can be implemented using ROMs
Also used in computer systems for initialization
  ROM doesn’t lose storage value when power is removed
Very useful for implementing FSMs
6
2k x n ROM
  k address input lines
  enable input(s)
  three-state outputs
Notes: credential:
bring a computer
die photo
wafer
:
This can be an hidden slide. I just want to use this to do my own planning.
I have rearranged Culler’s lecture slides slightly and add more slides. This covers everything he covers in his first lecture (and more) but may
We will save the fun part, “ Levels of Organization,” at the end (so student can stay awake): I will show the internal stricture of the SS10/20.
Notes to Patterson: You may want to edit the slides in your section or add extra slides to taylor your needs.

## Slide 7: ROM Structure
.
.
.
k Inputs
k x 2k
decoder
...
n Outputs Lines
.
.
.
Memory Array
2k words x n bits
7

## Slide 8: A 32 x 8 ROM
8
  5-to-32 decoder
  8 OR gates
    each has 32 inputs
  32x8 internal programmable connections

## Slide 9: A ROM Example
9
(0)
(1)
(2)
(3)
(28)
(29)
(30)
(31)
(address)
…

## Slide 10: A ROM Example
(From Table 7-3 )
10

## Slide 11: Types of ROM
  Mask programming ROM
    IC manufacturers
    is economical only if large quantities
  PROM: Programmable ROM
    fuses
    universal programmer
  EPROM: erasable PROM
    floating gate
    ultraviolet light erasable
  EEPROM: electrically erasable PROM
    longer time is needed to write
    flash ROM
    limited times of write operations
11

## Slide 12: Random-Access Memory

## Slide 13: Block Diagram of a Random-Access Memory (RAM)
Data input and output lines carry data
Memory contains 2k words
  k address lines select one word out of 2k
Read asserted when data to be transferred to output
Write asserted when data input to be stored
13

## Slide 14: Write and Read Operations
Write operation
  Apply the binary address to the address lines
  Apply the data bits to the data input lines
  Activate the write input
Read operation
  Apply the binary address to the address lines
  Activate the read input
14

## Slide 15: Timing Waveform – Write Operation
15
The write cycle time is the maximum time from the application of the address to the completion of all internal memory operations required to store a word.
Assume, as an example, that a CPU operates with a clock frequency of 50 MHz, giving a period of 20 ns. A write cycle time is 75 ns.
Apply binary address of word to address lines
Apply data bits to data input lines
Activate write input

## Slide 16: Timing Waveform – Read Operation
16
The access time of a memory read operation is the maximum time from the application of the address to the appearance of the data at the Data Output.
An access time is 65 ns.
Apply the binary address to the address lines
Activate read input

## Slide 17: Comments about Memory Access and Timing
Most computers have a central processing unit (CPU)
  Processor generates control signals, address, and data
  Values stored and then read from RAM
The timing of the system is very important.
  Processor provides data for the cycle time on writes
  Processor waits for the access time for reads
17

## Slide 18: Types of Random Access Memories
Static random access memory (SRAM)
  Operates like a collection of latches
  Once value is written, it is guaranteed to remain in the memory as long as power is applied
  Generally expensive
  Used inside processors (like the Pentium)
Dynamic random access memory (DRAM)
  Generally, simpler internal design than SRAM
  Requires data to be rewritten (refreshed), otherwise data is lost
  Often hold larger amount of data than SRAM
  Longer access times than SRAM
  Used as main memory in computer systems
18

## Slide 19: Static RAM Cell
19
We first show a static RAM cell for storing a single bit and then use the cell in a hierarchy to describe the RAM chip
  SR Latch
  Select input for control
  Dual Rail Data Inputs B and B
  Dual Rail Data Outputs C and C

## Slide 20: Static RAM Bit Slice
20
Represents all circuitry that is required for 2n 1-bit words

## Slide 21: Static RAM Bit Slice
21
The loading of a cell latch is now controlled by a Word Select input.
  If this is 0, then both S and R are 0, and the cell latch contents remain unchanged.
  If this is 1, then the value to be loaded into the latch is controlled by two signals B and B from the Write Logic
  Read/Write must be 0 and Bit Select must be 1
  If Data In is 1, the latch is set to 1
  If Data In is 0, the latch is reset to 0, completing the write operation
The Word Select also controls the reading of the RAM cells, using shared Read Logic.
  If this is 0, the stored value in the SR latch is prevented by the AND gates from reaching the pair of OR gates in the Read Logic.
  If this is 1, the stored value passes through to the OR gates and is captured in the Read Logic SR latch.
  If Bit Select is also 1, the captured value appears on the Data Out line of the RAM bit slice.

## Slide 22: A 16 x 1 RAM chip
22
The Chip Select at the chip level corresponds to the Memory Enable at the level of a RAM consisting of multiple chips.

## Slide 23: Cell Arrays and Coincident Selection
23
Inside a RAM chip, the decoder with k inputs and 2k outputs requires 2k AND gates.
The decoder size and fanouts can be reduced by approximately by using a coincident selection in a 2-dimensional array.
  Uses two decoders, one for words and one for bits
  Word select becomes Row select
  Bit select becomes Column select

## Slide 24: Block Diagram of a 16x1 RAM Using a 4x4 RAM Cell Array
24

## Slide 25: Block Diagram of a 8x2 RAM Using a 4x4 RAM Cell Array
25

## Slide 26: Block Diagram of a 256K x 8 RAM
26

## Slide 27: Block Diagram of a 64K x 16 RAM
27

## Slide 28: Dynamic RAM (DRAM)
28
Basic Principle: Storage of information on capacitors.
Charge and discharge of capacitor to change stored value.
Need periodically “refreshed.
Use of transistor as “switch” to:
  Store charge
  Charge or discharge

## Slide 29: DRAM Cell
29
Small tank is initially high (1)
Small tank is initially low (0)
Write 1:
Pumps fill up the large tank.
Water flows through the valve,
fill the small storage tank
Write 0:
Pumps empty the large tank.
Water flows through the valve,
empty the small storage tank

## Slide 30: DRAM Cell
30
Read 1:
Start with a full storage tank.
Large tank at a known intermediate level.
Open the valve, water flows from the small tank to the large tank.
Increasing the level of the water surface in the large tank slightly.
This increase in level is observed as the reading of 1 from the storage tank.
Read 0:
Start with an empty storage tank.
Large tank at a known intermediate level.
Open the valve, water flows from the large tank to the small tank.
Decreasing the level of the water surface in the large tank slightly.
This decrease in level is observed as the reading of 0 from the storage tank.
a logic DRAM cell model, which is a D latch.

## Slide 31: DRAM Bit Slice
31

## Slide 32: Timing Waveform – Write Operation
32
The row address is applied, RAS changes from 1 to 0.
The column address is applied, CAS changes from 1 to 0.
The input data with Read/Write = 0 is applied over a time interval similar to that for the column address.

## Slide 33: Timing Waveform – Read Operation
33
The row address is applied, RAS changes from 1 to 0.
The column address is applied, CAS changes from 1 to 0.
The input data with Read/Write = 1 is applied, selected value
is sent to the Data output, which is enabled by Output enable.

## Slide 34: DRAM Types
34