## Slide 1: LCD Display

## Slide 2: Outline
LCD (Text)
LCD_Keypad
LCD_Bmp
LCD_Bmp_Keypad
LCD_Graph_2D
LCD_Graph_PingPong
SampleCode Projects to cover:
2

## Slide 3: Pins to drive LCD
GPD8-GPD11 to control LCD
3

## Slide 4: LCD Display Introduction
種類
  文字型：已經有內建文字圖形（通常只有英文字母大小寫、阿拉伯數字、標點符號），只要輸入對應的字形碼（ASCII code），LCD便會將該字的圖形顯示於LCD.
  繪圖型：用繪圖的方式將資料顯示於LCD. 必須先將要顯示文字的圖形依LCD所需的格式事先存起來，再將此資料依序填入LCD即可顯示對應圖形.
基本知識
  LCD 裡面是兩片玻璃中間夾液晶， 上面有透明的導電線路(特殊材質) ，下面也有，上面的叫做 Segment ，下面的叫做 Common.
  LCD 上的圖形是否被點亮是由Segment 和 Common 之間的電壓差決定.
4

## Slide 5: UC1601 Controller
Nu-LB-NUC140 Learning Board uses UC1601 controller to transfer data between MCU and LCD.
UC1601 block diagram:
5

## Slide 6: LCD Layout: Text
6
LCD可以顯示4列，每列16字元
……………………….
……………………….
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
(X,Y)Text
(0,0)
(15,0)
(15,3)
(0,3)

## Slide 7: LCD Layout: Bitmap
7
(0,0)
(0,63)
(127,63)
(127,0)
LCD可以顯示 128 x 64 = 8192 pixels
……………………….
……………………….
………………………………...
(X,Y)Bitmap

## Slide 8: LCD Function Calls (LCD.h)
8
#define LCD_Xmax 128
#define LCD_Ymax 64
#define FG_COLOR 0xFFFF
#define BG_COLOR 0x0000
init_LCD();  initialize LCD display
clear_LCD();  clean up LCD display
printC(x, y, ascii_code);  print a character using font8x16 on LCD at location (x,y)
printC_5x7(x, y, ascii_code);  print a character using font 5x7 on LCD at location (x,y)
print_Line( line, text[]);  print a string (maximum = 16 charactors) on LCD (line no = 0,1,2,3)
printS(x, y, text[]);  Print a string using font 8x16 on LCD at location (x,y)
printS_5x7(x, y, text[]);  print a string using font 5x7 on LCD at location (x,y)
draw entire LCD (128x64 pixels)
Print Text

## Slide 9: LCD Function Calls (LCD.h)
9
extern void draw_Bmp8x8(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp32x8(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp120x8(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp8x16(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x8(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x16(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x24(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x32(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x40(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x48(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp16x64(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp32x16(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp32x32(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp32x48(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp32x64(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Bmp64x64(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor, unsigned char bitmap[]);
extern void draw_Pixel(int16_t x, int16_t y, uint16_t fgColor, uint16_t bgColor);
extern void draw_LCD(unsigned char *buffer);
Draw Bitmap

## Slide 10: SampleCode: LCD
10

## Slide 11: SampleCode: LCD_Keypad
11

## Slide 12: An Example
12

## Slide 13: UC1601 Controller
Command Table
13

## Slide 14: UC1601 Controller
Display Data Ram
14
Page 0, SEG 1: 00011111b
Page 0, SEG 2: 11001100b
common
drivers
……
…………
segment
drivers
……………….

## Slide 15: ASCII Code for Charactors
15
/* A */
0x00,0x00,0x80,0x70,0x80,0x00,0x00,0x00,0x80,0xF0,0x8F,0x08,0x8F,0xF0,0x80,0x00,
Page n
Page n+1

## Slide 16: LCD.c
16

## Slide 17: LCD.c
17

## Slide 18: LCD.c
18

## Slide 19: LCD.c
19

## Slide 20: Generate Hex of Bitmap
20
Step 1. use 小畫家 to draw a 128x64 bitmap
Step 2. use bmp2asm to convert bitmap into
hex
Step 3. cut and paste hex of bitmap to
display buffer in your program.

## Slide 21: SampleCode: LCD_Bmp
21
………

## Slide 22: LCD.c
22
Set X coordinate and Y page to LCD register
Display Data write to LCD

## Slide 23: Whole Bitmap Display
23
pixel at (3,9)
(draw_Pixel)
a byte data at xi
(draw_LCD)
x0
x1
x127

## Slide 24: SampleCode: LCD_Bmp_Keypad
24

## Slide 25: LCD.c
25

## Slide 26: 16x16 Bitmap Display
26
pixel at (kx,ky)
(draw_Pixel)
a byte data at t
(draw_Bmp16x16)
t
16 x 16

## Slide 27: SampleCode: LCD_Bmp_Keypad (cont.)
27
1
2
3
4
5
6
7
8
9

## Slide 28: Animation flow chart
28
Draw Object/Bitmap
on LCD Display
Delay for Vision
Erase Object/Bitmap
from LCD Display
X, Y increment/decrement
Check Boundary

## Slide 29: Draw Objects
29
draw_Circle(x, y, r, fgColor, bgColor);
Or
draw_Bmp16x16(x, y, fgColor, bgColor, bitmap);
Draw a circle at x,y using foreground color

## Slide 30: Display Objects
30
Delay for Vision (視覺暫留)
CLK_SysTickDelay(100000);

## Slide 31: Erase Objects
31
draw_Circle(x, y, r, bgColor, bgColor);
Or
draw_Bmp16x16(x, y, bgColor, bgColor, bitmap);
Draw a circle at x,y using background color

## Slide 32: SampleCode: LCD_Graph_2D
32
Bresenham Line-Drawing Algorithm
Bresenham Circle-Drawing Algorithm

## Slide 33: Bresenham Line-Drawing Algorithm
33
https://www.javatpoint.com/computer-graphics-bresenhams-line-algorithm
The big advantage of this algorithm is that, it uses only integer calculations.
Moving across the x axis in unit intervals and at each step choose between two different points, that is (xk+1, yk+1) or (xk+1, yk).
Line equation :
y=mx+b, where m =

## Slide 34: Bresenham Line-Drawing Algorithm
34
True line
The actual y coordinates of the line at xk+1is y = mxk+1+b = m(xk + 1)+b
s = y-yk
t = (yk+1)-y
When (s-t) <0 ⟹ s < t, the closest pixel is yk
When (s-t) ≥0 ⟹ s ≥ t, the closest pixel is yk+1
This difference is s-t = (y-yk)-[(yk+1)-y] = 2y - 2yk -1 = 2m(xk + 1) + 2b - 2yk -1
Substituting m by
, and introducing decision variable dk=△x (s-t)
dk=△x ( 2 (xk+1)+2b-2yk-1)) =2△y∙xk +2△y +△x∙2b - △x∙2yk - △x
=2△y∙xk - △x∙2yk + c, where c=2△y+△x (2b-1)

## Slide 35: Bresenham Line-Drawing Algorithm
35
If chosen pixel is at yk+1 (i.e., dk≥0)⟹ yk+1=yk+1
We can write the decision variable dk+1 for the next slip on
dk+1=2△y∙xk+1 - △x∙2yk+1 + c
dk+1- dk = 2△y(xk+1 - xk) - 2△x(yk+1 - yk)
Since xk+1= xk+1, we have
dk+1- dk = 2△y(xk+1 - xk) - 2△x(yk+1 - yk) = 2△y - 2△x(yk+1 - yk)
dk+1 = dk + 2△y - 2△x
If chosen pixel is at yk (i.e., dk<0)⟹ yk+1=yk
dk+1 = dk + 2△y
Initial case:
d1 = △x[2m(x1 + 1) + 2b - 2y1 -1] = △x[2(mx1+b-y1)+2m-1] = △x[2m-1]
= y1
d1 = 2△y -△x
Algorithm: read the draw_Line() code in Draw2D.c

## Slide 36
36
+

## Slide 37: Bresenham Circle-Drawing Algorithm
37
https://www.javatpoint.com/computer-graphics-bresenhams-circle-algorithm
Scan-Converting a circle using Bresenham's algorithm works as follows:
Points are generated from 90° to 45°
Moves will be made only in the +x & -y directions
Then extends them to the other 7 octants, by using the concept of eight-way symmetry.

## Slide 38: Bresenham Circle-Drawing Algorithm
38
P
Q
Each new point closest to the true circle can be found by taking either of two actions.
  Move in the x-direction one unit, point P =(xi+1, yi)
  Move in the x- direction one unit & move in the negative y-direction one unit, point Q =(xi+1, yi-1).
D(ti) is the distance to point P squared minus the distance from the origin to the true circle squared.
D(si) is the distance to point Q squared minus the distance from the origin to the true circle squared.
D(ti)=(xi+1)2+ yi2 - r2
D(si)=(xi+1)2+ (yi-1)2 - r2
≧ 0
≦ 0
A decision variable
di =D(ti)+D(si) = (xi+1)2+ yi2 - r2 + (xi+1)2+ (yi-1)2 - r2
If it is assumed that the circle is centered at the origin, then at the first step x = 0 & y = r.
d1 = (0+1)2+ r2 - r2 + (0+1)2+ (r-1)2 - r2 = 3 – 2r
Thereafter, if di<0, then only x is incremented.
if di≥0, then x & y are modified
xi+1=xi+1
di+1=di+ 4xi+6
xi+1=xi+1
di+1=di+ 4(xi-yi)+10
yi+1=yi-1

## Slide 39: Draw2D.c
39

## Slide 40: Draw2D.c
40

## Slide 41: SampleCode: LCD_Graph_2D
41

## Slide 42: SampleCode: LCD_Graph_PingPong
42

## Slide 43: SampleCode: LCD_Graph_PingPong
43

## Slide 44: SampleCode: LCD_Graph_PingPong
44