## Slide 1: Interrupt

## Slide 2: Polling vs Interrupt
2
Polling
  Waste CPU’s processing time and energy
  Most of the time, nothing changes
Interrupt
  Specific type of an exception
  Exception is a hardware-invoked subroutine call.
  Subroutine is called an Interrupt Service Routine (ISR) or Interrupt handler.
There are many ways to structure the flow of the application:

## Slide 3: Polling
3
Polling (sometimes also called super loop) is easy to set up and works fairly well for simple tasks

## Slide 4: Interrupt
4
Interrupts are usually generated by external sources or on chip peripherals to wake up the processor.

## Slide 5: Interrupt Basics
5

## Slide 6: Flow of an Interrupt
6

## Slide 7: Flow of an Interrupt
7

## Slide 8: What Happens on an Exception
8

## Slide 9: Exception Flow
9

## Slide 10: Nested Exceptions
10

## Slide 11: Pending Exceptions
11

## Slide 12: NVIC Control Registers
12

## Slide 13: System Interrupt Map
13

## Slide 14: System Interrupt Map
14

## Slide 15: GPIOs Generate Exceptions
15
GPIO pins can configured to generate exceptions (interrupts).
There are four types of interrupt condition can be selected: low level trigger, high level trigger, falling edge trigger and rising edge trigger.
For edge trigger condition, user can enable input signal de-bounce function to prevent unexpected interrupt happened which caused by noise.

## Slide 16: EINT1 on Learning board
16

## Slide 17: GPIO Interrupt pin setting
17
GPIO pin mode : Input
  GPIO_SetMode(PB, BIT15, GPIO_MODE_INPUT);
GPIO interrupt trigger type : RISING/FALLING/BOTH_EDGE/HIGH/LOW
  GPIO_EnableEINT1 (PB, BIT15, GPIO_INT_FALLING);
GPIO Interrupt :
  NVIC_EnableIRQ(EINT1_IRQn);
GPIO pin debouncing:
  Debounce Clock Source = LIRC (10KHz) or HCLK
  GPIO_SET_DEBOUNCE_TIME(GPIO_DBCLKSRC_LIRC, GPIO_DBCLKSEL_64);
  GPIO_ENABLE_DEBOUNCE(PB, BIT15);

## Slide 18: SampleCode: GPIO_ExtInt (with modification)
18
INT0 /PB14 : unstable, not recommended
INT1 /PB15 :

## Slide 19: GPIO Interrupt pin setting
19
GPIO pin mode : Input
  GPIO_SetMode(PA, BIT12, GPIO_MODE_INPUT);
GPIO interrupt trigger type : RISING/FALLING/BOTH_EDGE/HIGH/LOW
  GPIO_EnableInt(PA, BIT12, GPIO_INT_FALLING);
GPIO Interrupt groups: AB or CDE
  NVIC_EnableIRQ(GPAB_IRQn); // AB group share 1 interrupt to CPU
  NVIC_EnableIRQ(GPCDE_IRQn); // CDE group share 1 interrupt to CPU
GPIO pin debouncing:
  Debounce Clock Source = LIRC (10KHz) or HCLK
  GPIO_SET_DEBOUNCE_TIME(GPIO_DBCLKSRC_LIRC, GPIO_DBCLKSEL_64);
  GPIO_ENABLE_DEBOUNCE(PA, BIT12);

## Slide 20: SampleCode: GPIO_IRQ (with modification)
20
// wire PA12,13,14 to Ground will trigger interrupt
GND
PA12, PA13, PA14

## Slide 21: SampleCode: GPIO_IRQ (with modification)
21

## Slide 22: SampleCode: GPIO_IRQ (with keypad)
22
GPAB_IRQn
0
0
0

## Slide 23: SampleCode: GPIO_IRQ (with keypad)
23

## Slide 24: SampleCode: GPIO_IRQ (with keypad)
24