## Slide 1: Analog-to-Digital Converter (ADC)

## Slide 2: Outline
ADC_VR1
ADC_8ch
SampleCode Projects to cover:
2

## Slide 3: Signal Conversion
3
ADC
DAC
Filter

## Slide 4: Analog to Digital Conversion
4
Vin is input voltage for ADC to sample
Vref is reference voltage for ADC to compare with Vin
  Vref is connected to 3.3V on NUC140 learning board
12-bit ADC : output is a 12-bit binary code, so its value = 0 ~ 4095
Decimal | Binary | Voltage (Vref=3.3V)
0 | 0000_0000_0000 | 0/4096 * 3.3V
1 | 0000_0000_0001 | 1/4096 * 3.3V
2048 | 1000_0000_0000 | 2048/4096 * 3.3V
4095 | 1111_1111_1111 | 4095/4096 * 3.3V

## Slide 5: ADC Architectures
5
Direct-Conversion ADC
SAR (Successive Approximation Register) ADC
ΔΣ (Sigma-Delta) ADC
Direct-Conversion ADC
SAR ADC
Successive Approximation Register
Sigma-Delta ADC

## Slide 6: SAR (Successive Approximation Register) ADC
6
這一種ADC由一個DAC與電壓比較器組成，依序由MSB往LSB更改DAC的輸出電壓。
流程：
由MSB開始
啟動DAC的第n bit (DN-1)
將輸入的訊號與DAC的輸出做比較，若輸入訊號較大，則設定ADC輸出的第n bit為HIGH，並保留DAC上面的設定，反之若較小，清除DAC的第n bit，並設定ADC輸出的第n bit為LOW
由這一個狀態迭代至LSB(D0)為止

## Slide 7: NUC140 ADC
Contain one 12-bit successive approximation analog-to-digital converters (SAR A/D converter) with 8 input channels.
The A/D converter supports three operation modes: single, single-cycle scan and continuous scan mode.
Overview
7
Analog input voltage range: 0~Vref (Max to 5.0V).
12-bit resolution and 10-bit accuracy is guaranteed
Input channel:
  Up to 8 single-end analog input channels
  4 pairs of differential analog input channel
The maximum ADC operating frequency is 16M Hz
Three ADC operation modes
  Single mode
  Single-cycle mode
  Continuous mode
An A/D conversion can be started by
  Software write 1 to ADST bit
  External pin STADC
Features

## Slide 8: NUC140 ADC Block Diagram
8

## Slide 9: NUC140 System Interrupt Map
9

## Slide 10: ADC Clock Source
10
The maximum sampling rate is up to 700K SPS (Samples Per Second)
The ADC engine has four clock sources selected by 2-bit ADC_S (CLKSEL1[3:2]).
ADC clock frequency is divided by an 8-bit prescaler with the formula:
  The ADC clock frequency = (ADC clock source frequency) / (ADC_N+1);
  ,where the 8-bit ADC_N is located in register CLKDIV[23:16].

## Slide 11: ADC Interrupt Sources
11
There are three interrupt sources of ADC interrupt
  When an ADC operation mode finishes its conversion, the A/D conversion end flag, ADF, will be set to 1
  When one of the flags, ADF, CMPF0 and CMPF1, is set to 1 and the corresponding interrupt enable bit, ADIE of ADCR and CMPIE of ADCMPR0/1, is set to 1, the ADC interrupt will be asserted

## Slide 12: Functional Description
12
Single Mode
A/D conversion is performed only once on the specified single channel
The operations are as follows:
  A/D conversion will be started when the ADST bit of ADCR is set to 1 by software or external trigger input.
  When A/D conversion is finished, the result is stored in the A/D data register corresponding to the channel. The ADF bit of ADSR register will be set to 1.
  If the ADIE bit of ADCR register is set to 1, the ADC interrupt will be asserted.
  The ADST bit remains 1 during A/D conversion. When A/D conversion ends, the ADST bit is automatically cleared to 0 and the A/D converter enters idle state.
Note: If software enables more than one channel in single mode, the channel with the lowest number will be selected and the other enabled channels will be ignored.

## Slide 13: Single Mode Conversion Timing Diagram
13

## Slide 14: Functional Description
14
Single-Cycle Scan Mode
A/D conversion will sample and convert the specified channels once in the sequence from the lowest number enabled channel to the highest number enabled channel.
The operations are as follows:
  When the ADST bit of ADCR is set to 1 by software or external trigger input, A/D conversion starts on the channel with the lowest number.
  When A/D conversion for each enabled channel is completed, the result is sequentially transferred to the A/D data register corresponding to each channel.
  When the conversions of all the enabled channels are completed, the ADF bit in ADSR is set to 1.
  If the ADC interrupt function is enabled, the ADC interrupt occurs.
  After A/D conversion ends, the ADST bit is automatically cleared to 0 and the A/D converter enters idle state

## Slide 15: Single-Cycle Scan Mode Conversion Timing Diagram
15
An example timing diagram for single-cycle scan on enabled channels (0, 2, 3 and 7)

## Slide 16: Functional Description
16
Continuous Scan Mode
A/D conversion is performed sequentially on the specified channels that enabled by CHEN bits in ADCHER register (maximum 8 channels for ADC)..
The operations are as follows:
  When the ADST bit of ADCR is set to 1 by software or external trigger input, A/D conversion starts on the channel with the lowest number.
  When A/D conversion for each enabled channel is completed, the result is sequentially transferred to the A/D data register corresponding to each channel.
  When the conversions of all the enabled channels are completed, the ADF bit in ADSR is set to 1.
  If the ADC interrupt function is enabled, the ADC interrupt occurs. The conversion of the enabled channel with the lowest number will start again if software has not cleared the ADST bit.
  As long as the ADST bit remains at 1, the above steps will be repeated.

## Slide 17: Continuous Scan Mode Conversion Timing Diagram
17
An example timing diagram for continuous scan on enabled channels (0, 2, 3 and 7)

## Slide 18: Timer Register Map
18

## Slide 19: NUC140 ADC Clock Selection (in SYS_init.c)
19
void CLK_SetModuleClock(
uint32_t u32ModuleIdx,
uint32_t u32ClkSrc,
uint32_t u32ClkDiv)
ADC Clock Source
CLK_CLKSEL1_ADC_S_HXT
CLK_CLKSEL1_ADC_S_PLL
CLK_CLKSEL1_ADC_S_HCLK
CLK_CLKSEL1_ADC_S_HIRC
ADC Clock Divider
CLK_CLKDIV_ADC(x)
Module Index = ADC
Clock Source
Clock Divider
ADC clock 8-bit divider = x

## Slide 20: ADC Initialization (in adc.c)
20
void ADC_Open(ADC_T *adc,
uint32_t u32InputMode,
uint32_t u32OpMode,
uint32_t u32ChMask)
ADC input mode
ADC_INPUT_MODE_SINGLE_END
ADC_INPUT_MODE_DIFFERENTIAL
ADC operation mode
ADC_OPERATION_MODE_SINGLE
ADC_OPERATION_MODE_SINGLE_CYCLE
ADC_OPERATION_MODE_CONTINUOUS
ADC struct pointer
ADC input mode
ADC operation mode
ADC channel

## Slide 21: SampleCode: ADC_8ch (Continuous Scan Mode)
21
check ADC interrupt flag
read ADC value
clear ADC interrupt flag

## Slide 22: SampleCode: ADC_8ch (Continuous Scan Mode)
22
CONTINUOUS
SINGLE_END
ADC_CH_0_MASK| … | ADC_CH_7_MASK

## Slide 23: Learning Board
23
VR1
ADC0~7(GPA0~7)
Learning Board
ADC reference voltage is VCC33 (3.3V)
The ADC input pins share with GPIO group A
The ADC input pins must be configured in input type

## Slide 24: SampleCode: ADC_VR1 (Single-Cycle Scan Mode)
24
ADC Flag for main loop to detect when ADC sample finished
and ADC interrupt is generated
Set ADC software flag when IRQ ocurrs

## Slide 25: SampleCode: ADC_VR1
25
SINGLE_CYCLE
SINGLE_END
ADC_CH_7_MASK
start ADC conversion
wait for ADC sampling finished & generate interrupt to set this flag to 1

## Slide 26: SampleCode: ADC_VR1+LCD
26
Modify from ADC_Photoresistor
Add LCD.h

## Slide 27: SampleCode: ADC_VR1+LCD
27
define in MCU_init.h

## Slide 28: SampleCode: ADC_VR1+LCD (MCU_init.h)
28

## Slide 29: Joystick
29
Joystick 搖桿為一個雙向的10K電阻器，隨著搖桿方向不同，電阻值會隨著改變。
搖桿使用5V供電時，原始狀態下X,Y讀出的電壓為2.5V 。
向下按搖杆，可以觸動一個開關，對外輸出 0 或 1 的數位訊號。

## Slide 30: ADC_Joystick
30
VRx : PA0
VRy : PA1
SW : PC0

## Slide 31: ADC_Joystick
31

## Slide 32: ADC_Joystick
32
define in MCU_init.h

## Slide 33: ADC_Joystick+LCD
33
Add LCD.h

## Slide 34: ADC_Joystick+LCD
34
In this case, QUASI mode is more stable than INPUT mode

## Slide 35: ADC_Joystick+LCD
35